## Slide 1: 16.885: Medium-Fidelity Solar Airplane MDO
Peter Sharpe
2/20/2020

## Slide 2: Key Question
We have two missions:
Track storm
Stationkeep (sizes aircraft, we only care about this)
What happens if you not only optimize the design of the aircraft, but you also optimize how and where you fly the aircraft?
There is diurnal cycling of power into the system; it’s likely that the optimal trajectory takes advantage of this
  Altitude cycling
  Airspeed cycling
  How much of a benefit is this?
How do you design a multipoint-optimized airplane? Is it worth it?

## Slide 3: Problem Formulation
Aircraft design is fundamentally an optimization problem:
Minimize:
With respect to:
Subject to:
, , ,
(),
Minimize:
With respect to:
Subject to:
, , , ,
,
Typical
Aircraft
Solar Aircraft
Coupled Design and Trajectory Optimization Problem:
  Highly multidisciplinary:
  Problem size (tens of thousands of nonlinear, nonconvex variables and constraints)
  The circle-closing problem!
Aerodynamics
Structures
Propulsion
Stability & Control
Trajectory/Dynamics (2D)
Weights
Power Systems
, , and
At hundreds of collocation points over a 24-hour modeling window
Automatic-differentiable framework!

## Slide 4: Models: Geometry
Object-oriented aircraft geometry stack built in Python
  Fully modular
  Wings, fuselages, airfoils
  Lofting, parameter calculation (volume, wetted area, etc.)
  Thin surface or solid
  3D Tri/quad surface meshing
Free variables
  Wing sizing (span, chord, taper, etc.)
  Tail sized by volume coefficients

## Slide 5: Models: Aerodynamics
Aerodynamics solved simultaneously at every collocation point
Options:
  Traditional lift/drag/moment accounting
  Fully nonlinear lifting-line model
    Coupled viscous effects (significant Reynolds effects)
    Local stall modeling, local forces
    Fuselage modeling (line source + doublet)
    ~50 ms runtime
  Vortex-lattice model
    ~150 ms runtime
All models:
  Simultaneous Analysis and Design (SAND)-compatible
  End-to-end automatic differentiable
    Optimization
    Stability derivatives, eigenmode analysis
    Higher-order gradients (operator space closed under differentiation)

## Slide 6: Models: Aerodynamics
Airfoil data
  MSES sweeps on MIT Supercloud
    Angle of attack, Reynolds number, Mach number
  CL, CD fits to finely capture transitional performance (, not the best metric, but fits are quite good)
  E216 and RAE2822 airfoils
E216 Airfoil: L/D Ratio

## Slide 7: Models: Atmosphere and Wind
Atmosphere
  1976 COESA model
  Pressure, temperature, density (derived), Sutherland viscosity
Wind speed
  Currently assumed to be constant at 29 m/s (global, year-round 99% winds @ 65kft, from Kevin Uleck)
Future models
  Obtained API keys for the ECMWF ERA5 database
    Global atmospheric data at kilometer-scale resolution going back 50 years
    9 petabytes of data!
  Dataset trimmed to the most-relevant 12 GB
  Work in progress: regression to altitude, time of day, and latitude
  Preliminary findings: 99% percentile wind speed over CONUS @ ~69 kft, July-Aug., is 19.5 m/s
Based on an analysis of 1.2M samples
0.08% of the 12 GB dataset!
Hunch: diurnal cycling of wind speed?
2 DoF noncentral distribution, MLE reg.

## Slide 8: Models: Power Systems
Implemented Ed Lovelace’s presentation
Key Assumptions
  Battery
    Cell specific energy: 265 Wh/kg (Odysseus)
    80% allowable depth of discharge (for reserve, cycling, voltage cliff)
    Battery pack is 70% cells by weight (module HW, BMS, pack installation, thermal management, case, etc.)
    Realizable specific energy: 148.4 Wh/kg
  Accounting for wire weight assuming 10 AWG aluminum wire
  Solar cells:
    Realizable efficiency: 20.5% (temp. effects, spectral losses, multi-junction effects, MPPT losses, etc., conservative case)
    Area density: 0.30 kg/m2 (Burton, conservative case)
  Irradiance
    Day of year, time of day, latitude, orbital eccentricity, incidence angle losses

## Slide 9: Models: Propulsion
Dynamic disc-actuator theory
  Propeller efficiency of 0.7
  Motor efficiency of 0.85
  Propeller diameter and number of propellers left as free variables
Propulsion mass
  Motor: 4140 W/kg (Burton)
    Motor mass doubled to account for mounting and installation weight (Raymer)
  Propeller mass:
    Curve fit to carbon fiber paramotor propellers (similar disc loading, though a bit smaller size)
  ESC mass:
    Scraped the Hobbyking ESC listings and ran curve fits to ESCs in the 8s 100A range

## Slide 10: Models: Weights
Weight Breakdown
  Payload (30 kg)
  Structures
    Structural mass fraction guess: 0.25 – 0.31 (baseline: 0.31, Odysseus)
  Propulsion
    Motor, propeller, motor mounts
  Power Systems
    Batteries (and associated hardware), solar panels (and associated hardware), wire weight
  Avionics
    Flight controller, sensors, communications, servos

## Slide 11: Models: Dynamics
300 equally-spaced collocation points across a 24-hour cycle
  Midpoint-method integration (second-order accurate)
  Convergence testing indicates >200 collocation points is sufficient
Speed/Flight Path Angle velocity parameterization
  Conserves energy more accurately than Cartesian parameterization
Angle of attack and thrust left as decision variables (hence, short-period modes neglected)
  Optimal control problem

## Slide 12: Optimization
Jacobian computed for objective and constraints, Lagrangian hessian computed via automatic differentiation
Passed into IPOPT, an open-source interior point solver
Problem (aerodynamics: “workbook” method):
  3009 variables, 6313 constraints, 21903 constraint-variable interactions
  Solves in 2.14 seconds
Problem (aerodynamics: nonlinear viscous lifting line method):
  3208 variables, 5013 constraints, 29603 constraint-variable interactions
  Solves in 147.8 seconds
  Would likely be much faster with a good preconditioner
Performance for Various Aerodynamics Models
How much does the aero model matter?
  Across a variety of different assumptions, the mean absolute difference in the objective function (TOGW) at the optimum is 1.1%

## Slide 13: Results
Day 1, solar noon
Day 2, solar noon
Dusk
Dawn
Ambient wind field
Trajectory
Altitude-constrained
Headway requirement

## Slide 14: Results
TOGW
  Two sets of tech assumptions:
    Conservative (assumptions listed previously)
    Optimistic
TOGW [kg], Conservative |  |  | 
 |  | Altitude Cycling? | 
 |  | No | Yes
Airspeed Cycling? | No | DNC* | DNC*
 | Yes | DNC* | 272.5
* DNC = “Does Not Close”
TOGW [kg], Optimistic |  |  | 
 |  | Altitude Cycling? | 
 |  | No | Yes
Airspeed Cycling? | No | 236.5 | 204.6
 | Yes | 163.2 | 108.7

## Slide 15: Results

## Slide 16: Results

## Slide 17: Results

## Slide 18: Results

## Slide 19: Results

## Slide 20: Takeaway
There are huge benefits for solar aircraft if you do coupled design and trajectory optimization!
Considerations:
  Winds (although we designed to 29 m/s, and the 99th percentile CONUS summer 24-hour wind speed @ 69 kft is around 19.5 m/s)
    Time-of-day effects could help or hurt
  Propeller advance ratio, RPM (solvable)
    Variable pitch, gearbox?
  Temperature is not an issue
  Stretching structural weight assumptions at the low end
  Ascent
Notes
  Solar panel efficiency & weight matters little compared to battery weight

## Slide 21: New Optimization Strategies: Motivation
Aircraft design is fundamentally an optimization problem:
Minimize:
With respect to:
Subject to:
, , ,
(),
Maximize:
With respect to:
Subject to:
, ,
,
Typical
Aircraft
Firefly
Challenges
  Highly multidisciplinary:
  Problem size (tens of thousands of variables and constraints)
  The circle-closing problem!
Aerodynamics
Structures
Propulsion
Stability & Control
Trajectory/Dynamics
Weights
Packaging/Deployment
, , and

## Slide 22: New Optimization Strategies: Motivation
Aerodynamics
Structures
Propulsion
Stability & Control
Trajectory / Dynamics
Weights
Packaging / Deployment
Geometry
Range
  The circle-closing problem!
Driving dependencies (just to 1st order!)
Guess and check?
  Scales very poorly…
We need to implicitly solve for all disciplines simultaneously!
Design loop! (Implicit)
Notes: Do not pass go, do not collect $200

## Slide 23: New Optimization Strategies: Why Do We Care?
With new methods, we can solve these complex problems extremely quickly.
  Fast enough for interactive design
Example Problem:
Firefly design optimization
  8 disciplines
  3910 variables
  8420 constraints
  34321 constraint-variable interactions
  Nonlinear, nonconvex
6.91 seconds to solve on a laptop.

## Slide 24: Backup: Why not use GPKit?
Similarities
  AD-accelerated optimization and GPKit are similar in that they are both optimization-first approaches to engineering design
  Performance on GP-compatible problems is identical in terms of results, nearly identical in terms of speed
    “Simple Wing” example from GPKit documentation:
      GPKit: 41.9 milliseconds
      AD: 32.9 milliseconds
Advantages of AD
  GPKit restricts you not only to convex problems but also to GP-compatible problems*
    Can be a huge pain
    Engineering time required to do this can defeat the purpose of a conceptual framework (speed)
  Extensibility to higher fidelity
    GP-compatibility is often not possible for anything higher than zeroth-order analysis
Disadvantages of AD
  (For nonconvex problems:) problem requires sensible order-of-magnitude initial guesses
  (For good performance:) variables, constraints, and objectives should be scaled sensibly
Notes:
  While it’s true that GPKit offers global optimality and no initial conditions, that’s purely a consequence of fitting a problem into a GP-compatible space. Same thing is true for AD solving a GP-compatible problem.
Nonconvex problems
Convex (or log-convex) problems
GP-compatible problems
*SP-compatibility allows solution of a particular type of nonconvex problem, but it doesn’t scale to large problems
Simplified Taxonomy of Optimization Problems
AD wins, even without home-field advantage!

## Slide 25: New Optimization Strategies: Framework Considerations
Flexible level of fidelity
  Low fidelity analyses are useful but insufficient, especially for aerodynamics in this case
    Shock formation, laminar-turbulent transition, combustion rates, etc. are highly nonlinear!
(Ideally) even capable of handling slightly nonconvex problems
“Curse of Dimensionality”
Gradient-based optimization is the only tractable approach to large problems
  Method of gradient calculation
    Computational complexity
    Quality
Dimensionality vs. Computational Cost
Figure reproduced from J. Martins, 2013, “A Very Short Course on Multidisciplinary Design Optimization”
Improvement here is the key!
Modern methods: second-order (Newtonish)

## Slide 26: Backup: What is Gradient-based Optimization?
Explain gradient based optimization vs gradient free

## Slide 27: Backup: Convexity
Convex and Nonconvex Functions
Figure reproduced from M. Vernacchia, “Modeling Compress. Aero. Of Aircraft in GPs”
Definitions (pick one):
If you pick any two points on the curve, the line segment that connects them never goes below the curve.
everywhere
Log-convexity
Many, but not all simple engineering models can be roughly approximated as log-convex
More complex models usually cannot

## Slide 28: Backup: A Comparison of Gradient Methods
 | Finite Difference | Symbolic Differentiation* | Analytical Derivatives* | Automatic Differentiation*
Description | Pick two points, draw a line: | Use a symbolic engine to compute an expression for the derivative (Wolfram-Alpha, Mathematica) | Hand-compute the derivatives and write separate code to compute them. | Create a computational graph, then chain-rule backwards through it.
Computational complexity in dimensions |  | , probably non-polynomial | Potentially , though can require a huge amount of work by hand | 
Exact down to machine precision | No**, usually to | Yes | Yes | Yes
Other Pros | Black-box compatibility | Simplifies expressions where possible |  | 
Other Cons | Sensitive to small changes in (e.g. adaptive-step ODE integration) | Memory usage Control flow (if/then, for loops, etc.) | In practice, requires an astronomical amount of development work | Generally requires operator overloading or code parsing
 | Finite Difference | Symbolic Differentiation* | Analytical Derivatives* | Automatic Differentiation*
Description |  | Use a symbolic engine to compute an expression for the derivative (Wolfram-Alpha, Mathematica) | Hand-compute the derivatives and write separate code to compute them. | Create a computational graph, then chain-rule backwards through it.
 |  | Yes | Yes | Yes
Other Pros | Black-box compatibility | Simplifies expressions where possible |  | 
Other Cons |  | Memory usage Control flow (if/then, for loops, etc.) | In practice, requires an astronomical amount of development work | Generally requires operator overloading or code parsing
* Unfortunately, the names associated with different methods are not universally accepted by all fields – however, the names listed here reflect dominant trends.
** Complex-step finite differencing or higher-precision arithmetic can alleviate the accuracy issue, but these options are even slower and may not be as supported by numerical libraries.
Method
Figure of Merit
Notes: Consider dropping the last two rows

## Slide 29: New Optimization Strategies: Automatic Differentiation
Automatic Differentiation (AD)
  A method for computing gradients
  Other names: “autograd”, “algorithmic differentiation”, “backpropagation” (machine learning)
  Highly related to “adjoint formulations” in the PDE world
Why do we care?
  Calculate the derivative with respect to ALL design variables for the cost of just one extra function call!
  Gradients at machine precision
  Higher-order gradients at same cost
    Rapid, precise curvature information pairs well with modern nonlinear SQP-like optimization methods
Dimensionality vs. Computational Cost
Figure reproduced from J. Martins, 2013, “A Very Short Course on Multidisciplinary Design Optimization”

## Slide 30: New Optimization Strategies: How does AD work
Basic ideas:
  Every function, no matter how complex, can be broken up into simple operators (, etc.)
  We can show this breakdown with a computational graph
  We can use the chain rule to carry derivatives through the graph
Function
Computational Graph
Let’s differentiate with respect to at , labeling values and first derivatives!
Product rule:
Two flavors of AD
  Forward mode
    Cost scales with # of inputs
  Reverse mode
    Cost scales with # of outputs

## Slide 31: New Optimization Strategies: How does AD work
You can make a differentiable graph for ANY function!
Static vs. dynamic computational graphs
  “tape”
  Control flow (if/then, for loops)
Forward vs. reverse mode
Computational graph of mass calculation for a solar-powered blimp

## Slide 32: New Optimization Strategies: How does AD work
Differentiable physics models

## Slide 33: New Optimization Strategies: How does AD fit in
Automatic differentiation is provided through various machine learning and optimal control libraries, each with advantages:
  PyTorch: fastest run speed, coupling first-order optimizers
  CasADi: ODE integrators, coupling to second-order optimizers
  JAX: fastest dev. speed; differentiates native NumPy code
Other factors
  Sparse matrix representations
  Loose cross-disciplinary constraints

## Slide 34: New Optimization Strategies: Missions Enabled

## Slide 35: New Optimization Strategies: Missions Enabled
More stuff about interesting trades, design philosophies, things we’re sensitive to, etc.